- The University of Lethbridge, Lethbridge, Alberta, Canada

- Remote sensing of forest fires and mountain pine beetle damage in the Rocky Mountains

- The University of Lethbridge Goniometer System 2

- BRDF representations for grass and litter in blue grama grassland in three spectral bands (60° solar zenith angle)

- The new Alberta Water and Environmental Sciences Building (AWESB) at the University of Lethbridge

- Space-based monitoring Alberta’s oil sands over time

- Sample of forty three overlaid spectra used to measure line parameters for P-branch transitions in CO2

Information Contact

Dr. Philippe M. Teillet

Department of Physics and Astronomy

University of Lethbridge

4401 University Drive W.

Lethbridge, Alberta T1K 3M4

Canada

p.teillet@uleth.ca

Overview

Introduction

The Remote Sensing Group (RSG) at the University of Lethbridge (UL) is composed primarily of faculty, students and other researchers from the Department of Geography and the Department of Physics and Astronomy.  The RSG also collaborates with imaging scientists at the UL in the fields of astronomy, medical imaging, image processing/computer science, and kinesiology.

Primary Research Areas

- Analysis of atmospheric trace gases

- Atmospheric correction of satellite image data

- Bidirectional reflectance properties of Earth surfaces

- Development of remote sensing applications in agriculture, rangeland, forestry, mountainous terrain, oil sands, water resources, etc

- Hyperspectral imaging / imaging spectrometry

- Image classification, texture analysis, and spectral mixture analysis

- Image processing and analysis methodologies

- Investigations of molecular structures

- Remote sensing laboratory and field analyses

- Remote sensing instrumentation (field/airborne/atmospheric sensors)

- Sensor radiometric calibration

- Topographic corrections of satellite image data

- Vegetation canopy reflectance modeling and inversion

Alberta Terrestrial Imaging Centre

The Alberta Terrestrial Imaging Centre (ATIC) is a partnership between the UL and Iunctus Geomatics Corporation, a Lethbridge-based company.  ATIC is a non-profit research and development company that produces tools for optical remote sensing applications.  It is involved in a variety of projects leading to technologies for image information extraction from hyperspectral and multispectral image data.

.Multi-Disciplinary Major in Remote Sensing

The University of Lethbridge is putting in place a new Multi-Disciplinary Major in Remote Sensing, combining the strengths of the university’s Department of Geography and Department of Physics and Astronomy.  The program is designed to prepare B.Sc. graduates for a broad spectrum of job opportunities as well as graduate education and research.

.New Alberta Water and Environmental Sciences Building

A new Alberta Water and Environmental Sciences Building (AWESB) opened in autumn 2008 on the University of Lethbridge campus.  It contains modern geographical and biological science laboratories, including a remote sensing laboratory, dedicated to cutting-edge inter-disciplinary water and environmental research.

Remote Sensing Group

Faculty

Craig Coburn, Department of Geography

Derek Peddle, Department of Geography

Adriana Predoi-Cross, Department of Physics and Astronomy

Karl Staenz, Department of Geography

Phil Teillet, Department of Physics and Astronomy

Adjunct Professors

Ron Hall, Department of Geography (Adjunct), Canadian Forest Service

Anne Smith, Department of Geography (Adjunct), Agriculture Canada

Research Assistants

Mark Gibb, Department of Geography

Aaron Glover, Department of Geography

Chris Jackson, Department of Geography

Julia Lindeman, Department of Geography

Kevin Nakonechny, Department of Geography

Xiaomeng Ren, Department of Physics and Astronomy

Shiyong Xu, Department of Geography

Graduate Students

Amr Ibrahim, Department of Physics and Astronomy

Deep Mazumdar, Department of Geography

Kean O’Shea, Department of Geography

Chad Povey, Department of Physics and Astronomy

Dave Rolfson, Department of Geography

Casey Vandenberg, Department of Geography

Undergraduate Research Assistants

Casey Leonard, Department of Geography

Weiming Liu, Department of Physics and Astronomy

Aaron Mullin, Department of Geography

Reba Murphy, Department of Physics and Astronomy

Steve Myshak, Department of Geography

Ryan Selk, Department of Geography

Brandon Southgate, Department of Geography

Laboratories and Instrumentation

Remote Sensing Laboratory

Various elements of UL remote sensing instrumentation have been consolidated in a laboratory on the second floor of the new Alberta Water and Environmental Sciences Building.  The atmospheric spectroscopy laboratory is located on the seventh floor of University Hall.

Suite of Spectroradiometric Instrumentation

Hyperspectral Instrumentation

- ASD Field Spec spectrometers (3): 3 350-2500, 3 350-2500HR, and Pro 350-2500P

- ASD RTS-3ZC Reflectance/Transmittance Integrating Sphere

- ASD mercury argon calibration source assembly ALZSOLO

- VNIR imaging spectrometers (2): Specim V10E / Hamamatsu C8484 / Specim mirror scanner

Sun Photometers

- Cimel CE-318 autonomous Sun-tracking photometers (2)

- Yankee Environmental Systems SPUV sun photometer

Other Field Instruments

- LAI-2000 plant canopy analyzer

- TRAC (Tracing Radiation and Architecture of Canopies) system

- Trimble TSCL and ProXRS DGPS receivers

- Pulnix AccuPiXEL cameras (6)

- HEMI digital hemispherical photography system

Airborne Multispectral Camera System

Field Goniometer System

The UL Goniometer System version II (ULGS-II) instrument has a unique design that incorporates a number of advancements over other goniometers used to support remote sensing.  The ULGS II uses a quarter circle positioning arc with a 2-m radius and no part of the apparatus touches the ground in the target area.  This new design reduces the weight of the apparatus, increases portability, allows positioning over a wider variety of surfaces, and facilitates significantly faster data acquisition.  ULGS-II incorporates a computer-controlled motor-driven instrument payload that rapidly samples target bidirectional reflectance distribution functions.

Atmospheric Spectroscopy Laboratory

An experimental facility has been established for laboratory spectroscopy of terrestrial and planetary atmospheric molecule studies.  The main instrument is a 3-channel home-made laser spectrometer, tuneable from 1.48 to 3.8 micrometers. A variable-temperature single-pass absorption gas cell was custom designed and built for the spectroscopic study of gases.  This setup allows us to carry out highly sensitive line shape studies and fundamental spectroscopic studies of molecular interactions.  Tuneable diode laser absorption spectroscopy has also been used to develop an instrument capable of high-accuracy measurements of greenhouse gases such as N2O, CO2, and CH4. The field-portable instrument can be deployed in remote locations and used for measuring greenhouse gas concentrations.

2008 Bibliography, University of Lethbridge Remote Sensing Group

Publications in Refereed Journals

Bannari, A., K.S. Khurshid, K. Staenz, and J. Schwarz, 2008, Potential of Hyperion EO-1 Hyperspectral Data for Wheat Crop Chlorophyll Content Estimation, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S139-S157.

Bergeron, M., A. Hollinger, K. Staenz, M. Maszkiewicz, R.A. Neville, S. Qian, and D.G. Goodenough, 2008, Hyperspectral Environment and Resource Observer (HERO) Mission, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S1-S11.

Brazile, J., R.A. Neville, K. Staenz, D. Schläpfer, L. Sun, and K.I. Itten, 2008, Toward Scene-based Retrieval of Spectral Response Functions for Hyperspectral Imagers Using Fraunhofer Features, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S43-S58.

Buckingham, R., and K. Staenz, 2008, Review of Current and Planned Civilian Space Hyperspectral Sensors for EO, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S187-S197.

Burton, P.J., M-A. Parisien, J.A. Hicke, R.J. Hall, and J.T. Freeburn, 2008, Large fires as agents of ecological diversity in the North American Boreal Forest, International Journal of Wildland Fire, 17: 754-767.

Case, B.S., and R.J. Hall, 2008, Assessing prediction errors of generalized tree biomass and volume equations for the boreal forest region of west-Central Canada, Canadian Journal of Forest Research, 38: 878 - 889.

Eddy, P.R., A.M. Smith, B.D. Hill, D.R. Peddle, C.A. Coburn, and R.E. Blackshaw, 2008, Hybrid Segmentation – Artificial Neural Network Classification of High Resolution Hyperspectral Imagery for Site-Specific Herbicide Management in Agriculture, Photogrammetric Engineering & Remote Sensing: Special Issue on Artificial Intelligence in Remote Sensing, 74(10): 1249-1257.

French, N.H.F., E.S. Kasischke, R.J. Hall, K.A. Murphy, D.L. Verbyla, E.E. Hoy, and J.L. Allen, 2008, Using Landsat data to assess fire and burn severity in the North American boreal forest region: an overview and summary of results, International Journal of Wildland Fire, 17: 443 – 462.

Hall, R.J., 2008, Editorial: LiDAR use in natural resource management, The Forestry Chronicle, 84(6): 791-794.

Hall, R.J., J.T. Freeburn, W.J. de Groot, J.M. Pritchard, T.J. Lynham, and R. Landry, 2008, Remote sensing of burn severity: experience from western Canada boreal fires, International Journal of Wildland Fire, 17: 476 – 489.

Hopkinson, C., L. Chasmer, and R.J. Hall, 2008, The uncertainty in conifer plantation growth prediction from multitemporal lidar datasets, Remote Sensing Environment, 112: 1168 - 1180.

Joss, B., R.J. Hall, D.M. Sidders, and T.J. Keddy, 2008, Fuzzy logic modeling of land suitability for hybrid poplar across the Prairie Provinces of Canada, Environmental Monitoring and Assessment, 141: 79-96.

Levesque, J., and K. Staenz, 2008, Monitoring Mine Tailings Re-vegetation Using Multi-temporal Hyperspectral Image Data, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S172-S186.

Merzouki, A., A. Bannari, P.M. Teillet, and D.J. King, 2008, Caractérisation géostatistique de la variabilité spatiale de l’humidité du sol à l’aide des cartes dérivées des données radar à synthèse d’ouverture de Radarsat-1, Canadian Journal of Remote Sensing, 34(4): 376-389.

Neville, R.A., L. Sun, and K. Staenz, 2008, Spectral Calibration of Imaging Spectrometers by Atmosphere Absorption Matching, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S29-S42.

Pacheco, A., A. Bannari, K. Staenz, and H. McNairn, 2008, Deriving Percent Crop Cover Over Agricultural Canopies Using Hyperspectral Remote Sensing, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S110-S123.

Peddle, D.R., R.B. Boulton, N. Pilger, M. Bergeron, and A. Hollinger, 2008, Hyperspectral Detection of Chemical Vegetation Stress: Evaluation for the Canadian HERO Satellite Mission, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S198-S216.

Predoi-Cross, A. C. Holladay, H. Heung, J.-P. Bouanich, G.Ch. Mellau, R. Keller, and D.R. Hurtmans, 2008, Nitrogen-broadened lineshapes in the oxygen A-Band: experimental results and theoretical calculations, Journal of Molecular Spectroscopy, Special Issue Dedicated to E. Cohen and H. Pickett, 251: 159-175.

Predoi-Cross, A., K. Hambrook, R. Keller, D. Hurtmans, C. Povey, H. Over, and G. Mellau, 2008, Spectroscopic Lineshape Study of the Self-Perturbed Oxygen A-Band, Journal of Molecular Spectroscopy, 248: 85-110.

Richter, N., K. Staenz, and H. Kaufmann, 2008, Spectral Unmixing of Airborne Hyperspectral Data for Baseline Mapping of Mine Tailings Areas, International Journal of Remote Sensing, 29(13-14): 3937-3956.

Shang, J., R.A. Neville, K. Staenz, L. Sun, B. Morris, and P. Howarth, 2008, A Comparison of Fully Constrained and Weakly Constrained Unmixing through Mine-Tailings Composition Mapping, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S92-S109.

Smith, A.M., G. Bourgeois, P.M. Teillet, J. Freemantle, and C. Nadeau, 2008, "A comparison of NDVI and MTVI2 estimating LAI using CHRIS imagery: A case study in wheat", Canadian Journal of Remote Sensing, 34(6): 539-5.

Soenen, S.A., D.R. Peddle, C.A. Coburn, R.J. Hall, and F.G. Hall, 2008, Improved topographic correction of forest image data using a 3-D canopy reflectance model in multiple forward mode, International Journal of Remote Sensing, 29(4): 1007 - 1027 [DOI: 10.1080/01431160701311333].

Sun, L., R.A. Neville, K. Staenz, and H.P. White, 2008, Automatic Destriping of Hyperion Imagery Based on Spectral Moment Matching, Canadian Journal of Remote Sensing, Special issue on Hyperspectral Remote Sensing, 34(S1): S68-S81.

Teillet, P.M., and X. Ren, 2008, Spectral band difference effects on vegetation indices derived from multiple satellite sensor data, Canadian Journal of Remote Sensing, 34(3): 159-173.

Wulder, M.A., J.C. White, M. Cranny, R.J. Hall, J.E. Luther, A. Beaudoin, D.G. Goodenough, and J.A. Dechka, 2008, Monitoring Canada’s forests Part I: Completion of the EOSD land cover project, Canadian Journal of Remote Sensing, 34: 549 – 562.

Xu, S., D.R. Peddle, C.A. Coburn, and S.W. Kienzle, 2008, Sensitivity of a Carbon and Productivity Model to Climatic, Water, Terrain, and Biophysical Parameter in a Rocky Mountain Watershed, Canadian Journal of Remote Sensing, 34(3): 1-14.

Conference Proceedings Publications

Benner, D.C., V.M. Devi, A. Predoi-Cross, A. R. W. McKellar, L. R. Brown, R. A. Toth.,  and C. E. Miller, 2008, Temperature Dependence of Air-Broadened Half Width and Pressure Shift Coefficients in the 30012(00001 Band of 12C16O2, Proceedings of the 10th International HITRAN Meeting, Boston, Massachusetts, USA, 25.

Hill, B.D., A. M. Smith, G. L. Larson, and T. Hulstein, 2008, Estimating agricultural land cover in southern Alberta using Neural Network Trees and SPOT satellite imagery,  Proceedings 45th Annual Alberta Soil Science Workshop, Lethbridge, Alberta, pp.96-100.

Hill, B.D., A. M. Smith, G. L. Larson, and T. Hulstein, 2008, Neural network trees and spot satellite imagery to Estimating agricultural land cover in southern Alberta, Proceedings of FarmTech 2008, Edmonton, Alberta, Abstract, pp.148.

Perron, I., M.C. Nolin, E. Pattey, A. Smith, and J. Liu, 2008, Delineation of Homogeneous soil zones using sol electrical conductivity, multi-polarization SAR and hyperspectral data, Proceedings of the 9th International Conference on Precision Agriculture, Denver, Colorado, on CD-ROM, x pages.

Predoi-Cross, A., 2008, Molecular spectroscopic studies for remote sensing of earth and planetary atmospheres, Proceedings of the International Conference on Spectral Line Shapes, American Institute of Physics, 15: 289-297.

Predoi-Cross, A., A.R.W. McKellar, and D. R. Hurtmans, 2008, High accuracy line profile study of transitions in the 30012 ← 00001 and 30013 ← 00001 bands of carbon dioxide, Proceedings of the International Conference on Spectral Line Shapes, American Institute of Physics, 15: 265-273.

Predoi-Cross, A., J-P Bouanich, F. Rohart, and D.R. Hurtmans, 2008, Xe-Broadened CO Line Shapes in the Fundamental Band at 349 K, Proceedings of the International Conference on Spectral Line Shapes, American Institute of Physics, 15: 178-181.

Predoi-Cross, A., R. Austin, S. Bhadra, J. McKenna, L.-H. Xu, and M. Steinitz, 2008, Proceedings of the 3rd IUPAP Conference of Women in Physics, American Institute of Physics, 1119: 95-96.

Rochdi, P. Eddy, K. Staenz, J. Zhang, and Ch. Lutz, 2008, Monitoring Rangeland Plant Community Composition Using Spectral Mixture Analysis of Hyperspectral Remote Sensing Data, Proceedings of SPIE, Cardiff, UK, 7110: 711023-1 to 711023-10.

# Rohart, F. G. Wlodarczak, and A. Predoi-Cross, Forme des raies d’absorption moléculaire: comment interpréter les écarts au profil de Voigt?, Compte-rendu du Colloque de la Division de Physique Atomique, Moléculaire et Optique de la Société Française de Physique, Journées de Spectroscopie Moléculaire, Lille, France, 275.

Rohart, F., G. Wlodarczak, and A. Predoi-Cross, 2008, Molecular absorption lineshapes: analysis of departures from Voigt profile, Proceedings of Atmospheric Spectroscopy and Applications 2008, Reims, France, pp.10-13.

Smith, A.M., G.L. Larson, and S.A. Woods, 2008, Developing diagnostic tools for nitrogen management in potatoes, Proceedings of FarmTech 2008, Edmonton, Alberta, Abstract, pp. 148.

Smith, A.M., G.L. Larson, and S.A. Woods, 2008, Developing diagnostic tools for nitrogen management in potatoes, Proceedings of the 45th Annual Alberta Soil Science Workshop, Lethbridge, Alberta, pp. 101-106.

Smith, M. A. H., D.C. Benner, V.M. Devi, and A. Predoi-Cross, 2008, Self- and Air-Broadening, Shifts, and Line Mixing in the (4 and (2 Bands of CH4, Proceedings of the 10th International HITRAN Meeting, Boston, Massachusetts, USA,  28.

Smith, M. A. H., V.M. Devi, D.C. Benner, and A. Predoi-Cross, Spectroscopy of Methane at 7.6 μm, Proceedings of  Atmospheric Spectroscopy and Applications 2008, Reims, France, 4 pages.

Teillet, P.M., 2008, Sensor Webs: A Geostrategic Technology for Integrated Earth Sensing, Proceedings of International Workshop on Sensing a Changing World 2008, Kooistra, L., and Ligtenberg, A., 2008 (Eds.), CGI Report CGI-08-005, Wageningen University and Research Centre, Wageningen, The Netherlands, ISSN 1568-1874, pp. 10-13.

Zhang, J., K. Staenz, P. Eddy, N. Rochdi, D. Rolfson, and A.M. Smith, 2008, Analysis of Spaceborne Hyperspectral Imagery for the Estimation of Fractional Cover of Rangeland Ecosystems, Proceedings of the XXIst ISPRS Congress (International Society for Photogrammetry and Remote Sensing), Beijing, China, pp. 377-382.

Zhang, J., K. Staenz, P.R. Eddy, N. Rochdi, D. Rolfson, and A.M. Smith, 2008, Analysis of spaceborne Hyperion imagery for the estimation of fractional cover of rangeland ecosystems, Proceedings of the XXIst ISPRS Congress (International Society for Photogrammetry and Remote Sensing), Beijing, China, pp. 377-382.

Contributions to Collected Works

Wulder, M.A., M. Cranny, R. Hall, J. Luther, A. Beaudoin, J. White, D. Goodenough, and J. Dechka, 2008, Satellite land cover mapping of Canada’s forests: The EOSD land cover project, pp. 21-30 in J.C. Campbell, K.B. Jones, J.H. Smith, and M.T. Koeppe. (Editors), Chapter 3 in North America Land Cover Summit, Published by the American Association of Geographers, Washington, D.C., USA. http://www.aag.org/books/nalcs/chapters/CH3.pdf.

External Reports

Avitabile, V., L.B. Marchesini, H. Balzter, M. Bernoux, A. Bombelli, R.J. Hall, M. Henry, B.E. Law, R. Manlay, L.G. Marklund, Y.E. Shimabukuro, 2008, Assessment of the status of the development of standards for the terrestrial essential climate variables: ECV T12: Biomass, GTOS (Global Terrestrial Observing System), Rome, 24 pp.

Coburn, C.A., 2008, Evaluating the Impacts of Cattle Wintering Sites on Riparian Ecosystems using Remote Sensing, Final Report, Prairie Farm Rehabilitation Administration, Agriculture and Agri-Food Canada, 20 pp.

Hall, R.J., A. Beaudoin, J.E. Luther, E. Arsenault, L. Guindon, D.E. Piercey, R. Skakun, and P. Villemaire, 2008, Taking stock of Canada’s forests for Canadians: mapping biomass carbon stocks with satellite remote sensing data, Natural Resources Canada, Canadian Forest Service, Project Final Report to Canadian Space Agency (Project IMOU: 06MOA64836), 53 pp.

Hall, R.J., R.S. Skakun, and E.J. Arsenault, 2008, Multi-sensor remote sensing data for forest inventory: extending the value of satellite land cover maps, Canadian Forest Service, Natural Resources Canada, Project Progress Report to Government of Northwest Territories, 93 pp.

Smith A.M., 2008, Developing diagnostic tools for nitrogen management in potatoes, Final Report to the Potato Growers of Alberta, 21 pp.

2008 Professional Activities, University of Lethbridge Remote Sensing Group

Conferences, Workshops and Specialist Meetings

- 10th Annual Scientific Conference, Geomatics for Informed Decisions (GEOIDE) Network, Niagara Falls, Ontario, May 2008.

- 10th International HITRAN Meeting, Boston, Massachusetts, USA

- 19th Meeting of the Infrared Visible Optical Sensors (IVOS) Subgroup, Working Group on Calibration and Validation (WGCV), international Committee on Earth Observation satellites (CEOS), Tempe, Arizona, USA

- 2008 HYSPIRI Science Workshop, NASA-JPL, Monrovia, California, USA.

- 20th  International Conference on High Resolution Molecular Spectroscopy, Prague, Czech Republic

- 20th Meeting of the Infrared Visible Optical Sensors (IVOS) Subgroup, Working Group on Calibration and Validation (WGCV), Committee on Earth Observation satellites (CEOS), Tsukuba, Ibaraki, Japan

- 29th Canadian Symposium on Remote Sensing/10th International Circumpolar Remote Sensing Symposium, Whitehorse, Yukon

- 2nd International Spaceborne Imaging Spectroscopy (ISIS) Working Group Meeting, Boston, Massachusetts, USA.

- 3rd  Meeting of the EnMAP Scientific Advisory Group, German Aerospace Centre, Bonn, Germany

- 3rd IUPAP Conference of Women in Physics, Seoul, Korea

- 63rd Ohio State University International Symposium on Molecular Spectroscopy, Columbus, Ohio, USA

- 91st Canadian Chemistry Conference and Exhibition, Special Symposium dedicated to Mike Gerry, Edmonton, Alberta

- Annual Alberta Soil Science Workshop, Lethbridge, Alberta

- Atmospheric Spectroscopy and Applications 2008, Reims, France

- Canadian Association of Physicists Congress, Quebec City

# Colloque de la Division de Physique Atomique, Moléculaire et Optique de la Société Française de Physique
Journées de Spectroscopie Moléculaire, Lille, France

- FarmTech 2008, Edmonton, Alberta

- IEEE International Geoscience and Remote Sensing Symposium 2008, Boston, Massachusetts, USA.

- Impacts of fire and disturbance on carbon cycling in Western North America Workshop, NASA sponsored study on Regional Scale Studies of the Carbon Cycle science: Analyzing impacts of disturbances from insects and fire on the terrestrial carbon budget for the forested ecoregions of Canada, Alaska, and western US, Victoria, British Columbia

- International Conference on Spectral Line Shapes, Valladolid, Spain

- International Workshop on Sensing a Changing World, Wageningen University and Research Centre, Wageningen, The Netherlands

- Monitoring Trends in Burn Severity Workshop, US Geological Survey, Anchorage, Alaska

- SPIE Conference on Sensors, Systems, and Next-Generation Satellites XII, Cardiff, Wales, United Kingdom

- Workshop on Riparian Assessment and Monitoring at Watershed Scales, North Saskatchewan Watershed Alliance, Edmonton, Alberta, Canada

Service Activities and Memberships

- Airborne PRISM Experiment (APEX) Scientific Committee for the Design and Development of the Airborne PRISM (Process Research by an Imaging Space Mission) Simulator,  European Space Agency

- Alberta Geomatics Association

- Alberta Ingenuity Graduate Scholarship Committee-Physical Sciences Panel

- American Society of Agronomy

- American Society of Photogrammetry and Remote Sensing

- Canadian Association of Physicists

- Canadian Institute of Forestry

- Canadian Remote Sensing Society

- Co-chair, IEEE International  Spaceborne Imaging Spectroscopy (ISIS) Working Group

- College of Alberta Professional Foresters

- Editorial Board, Canadian Journal of Forest Research

- Editorial Board, Canadian Journal of Remote Sensing

- Editorial Board, Remote Sensing of Environment

- Editorial Board, The Forestry Chronicle

- Environmental Mapping and Analysis Program Scientific Advisory Committee (EnSAG) for a spaceborne hyperspectral mission, German Aerospace Centre, Germany

- Guest Editor, Special issue honouring molecular spectroscopists at the University of New Brunswick, Canadian Journal of Physics

- Guest Editor, Special issue on hyperspectral remote sensing, Canadian Journal of Remote Sensing

- International Organizing Committee of the International Conference on Spectral Line Shapes

- Organizing Committee, 29th Canadian Symposium on Remote Sensing, Whitehorse, Yukon

- President, Canadian Remote Sensing Society

- Research Management Committee (RMC), Geomatics for Informed Decisions (GEOIDE) Centre of Excellence, Canadian Networks of Centres of Excellence (NCE)

- Research Management Committee, Centre for Earth and Environmental Technologies, Ontario Centres of Excellence

- Secretary/Treasurer, Canadian Remote Sensing Society

- Subgroup on Infrared-Visible Optical Sensors (IVOS), Committee on Earth Observation Satellites (CEOS) Working Group on Calibration and Validation

- Technical Program Committee, 29th Canadian Symposium on Remote Sensing, Whitehorse, Yukon

- Technical Program Committee, ASTRO 2008 Conference, 2008, Montreal, Quebec

- Technical Program Committee, IEEE International Geoscience and Remote Sensing Symposium 2008, Boston, Massachusetts, USA.

- Technical Program Committee, SPIE Conference on Remote Sensing for Environmental Monitoring, GIS Applications, and Geology, Cardiff, Wales, UK

Courses Taught

- Department of Physics and Astronomy, University of Lethbridge

  - Introduction to Biophysics, Laboratory, Physics 1050

  - Physics of Remote Sensing, Physics 4650/5650/7651

  - Waves, Optics and Sound, Physics 2130

- Department of Geography, University of Lethbridge

  - Advanced Computer Mapping, Geography 4700

  - Advanced Remote Sensing, Geography 4725/5725

  - Cartography, Geography 3700

  - Geographic Data and Analysis, Geography 2700

  - Introduction to Geographical Information Systems, Geography 3740

  - Introduction to Geography, Geography 1010

  - Introduction to Remote Sensing, Geography 3720

  - Seminar in Geographical Information Systems, Geography 4752

  - Seminar in Remote Sensing, Geography 4753

  - Seminar in Spatial Modelling, Geography 4751

- 2-day Lecture on “National Security Using Hyperspectral Remote Sensing” to the Cabinet Satellite Intelligence Centre of the Government of Japan